## Slide 1
64-Tap 16-bit Dual-Clock Fixed-to-Floating-Point Finite Impulse Response Filter Design
CSEE W4823 Fall 2024 Project
Group 9
Yuan Jiang ( yj2848 )
Hongxin Xu ( hx2389 )

## Slide 2
Inputs:
  Provides clk1 (10 kHz) and clk2 (640 kHz) clock signals.
  Generates input stimulus din (16-bit FX) and preloads coefficients (16-bit FX) into memory from Matlab .txt files.
Top-Level FIR Core Modules:
  FIFO: Stores input data at clk1 and bridges asynchronous clock domains with clk2.
  CMEM: Pre-loaded 64 coefficients.
  IMEM_reg: Holds the 64 most recent input samples for convolution.
  ALU: Performs MAC and converts FX16 to FP16.
  FSM: Controls the states: IDLE, LOAD_COEF, PROCESS, and DONE.
Outputs:
  The filtered output dout (FP16) is generated and validated using valid_out signal.
  Compares outputs with precomputed values (.txt file).
  Flags mismatches and tracks error count / accuracy.
Architecture - FIR core Testbench

## Slide 3
Metrics of the FIR Filter
Metrics | Results
Throughput | 10 kS/s
Maximum Clock Frequency | 34.03 MHz
Power Consumption | 1.868 × 10-5 W
Energy Efficiency | 0.549 pJ/S
Area | 86547.7 mm2
Accuracy | Worst case: 95.30189 % ¦ Average: 99.92025 %
Methods source: Lecture 07, "Advanced Logic Design," Fall 2024 CSEE W4823, by Prof. Mingoo Seok, pp.9.